Problem 1: OSI model 3 points
Name the layers of the OSI model starting from the top and their general (most important) functions.

Application layer – provides standard protocol that can be used from applications
Presentation layer – represents the data depending on the hardware, Data are encoded in an abstract data format before the transmission
Session layer – manages reliable data transport between the computers, offers dialogue control, handles the token management and synchronisation points
Transport layer – manages end-to-end communication between two processes, ensures that data are receipt completely and in correct order, monitores current network state to adapt to the receiver and the network capacity (uses flow control), handles addressing
Network layer – responsible for data transmission over large distances and between heterogenous sub-networks, uniform addressing of hosts, routing, handles quality of service issues
Data Link layer – ensures error-free data transmission between two directly connected devices, data are segmented into frames, receiver checks correctness, flow control (re-transmission, protection from overload), control of medium access (prevent access conflics)
Physical layer – transmitting single bits, defines details (type of cables, meaning of pins, transmission direction)

Problem 2: Bridges and Switches 3 points
What layer of the OSI reference model do bridges and switches operate?

Bridges and switches mainly work on the data link layer. They can also work on the network layer if they have the capability to route between networks (IP switches).

Problem 3: Link Layer 3 points
What is controlled at the link layer?

It controls the segmentation of data into frames. The checksums are controlled. The flow is controlled so corrupt frames can be transmitted again. The medium access is controlled to prevent access control. It is also responsible for the logical link control data communication protocol to provide multiplexing mechanisms.

Problem 4: Overhead 3 points
Explain which service type has more overhead - connection-oriented or connection-less communication?

The connection-oriented communication has more overhead because of the required communication context. The establishment and termination of a connection is a overhead compared to the connection-less service. Furthermore there needs to be a negotiation of the protocol parameters.
On the other hand every data package sent via a connection-less communication needs things like a source address, destination address and other parameters.

Problem 5: Communication Principles 3 points
Explain the differences of unicast, multicast, anycast, and broadcast transmissions. Give an example application for each transmissions type.

- Unicast: communication of two peers over a point-to-point connection.
  e.g.: LAN-wire
- Multicast: one sender communicates to several receivers which are known.
  e.g.: a video server sending out networked TV channels
- Broadcast: one sender transmits to all other peers (unknown)
  e.g.: send an address resolution query to all computers on a LAN

Do you know what a concast and geocast is?

Yes. Does that answer the question?
Concast: Packets have a unicast destination address and a group source address. The concast addresses may only be used in the source field. Any host can send from the concast group so packets are merged in the network.
Geocast: information is delivered to a network which is identified by its geographical location. This is a specialized form of multicast.

What is the difference between a broadcast and flooding?

Sending a packet to all host simultaneously is broadcasting. Flooded packets will reach all nodes – this could send the same packet multiple times while broadcast will send a package at most once. Unlike flooding, broadcasting is done by specifying a broadcast address.

Problem 6: Cost efficient network upgrade 2+3 = 5 points

1. Given the network architecutre shown in Figure 1, what is the maximum network throughput when all clients access random servers in parallel?

The maximum network throughput is 100MBit/s due to the bottleneck between a and b. All clients need to access b via a in order to get to the server. This limits the throughput.

2. You could upgrade the 100 MBit/s connections to 1 GBit/s. However, you wonder if you could achieve a significant speed up with only upgrading a few connections. Is this possible? How big is the speed up?

Upgrading the connection from a to b would increase the total throughput to 200 MBit/s which would double the initial value.
A further upgrade of the connections from a to d and a to c would move the bottleneck to the connection from b to the server. The clients could request 1 GBit/s in total (10 x 100 MBit/s) but the connections from b to A, B and C could only handle 300MBit/s in the best case that the server requests are equally distributed. The throughput would be capped by this but would still be three times as high as the initial value.
An upgrade of the b – server connections to 1 GBit/s cables would give every client 100MBit/s. So the total network throughput would raise to 1GBit/s which is ten times as much as it was initially.
This is based on the assumption that all devices can handle that much throughput and that many requests.