Problem 5.1: Multiplexing and Multiple Access	2+2 = 4 points
• Discuss the terms multiplexing and multiple access and give examples.
Multiplexing is the sharing of a resource so it can be transferred or accessed faster. Multiple
signals are combined into one signal over a shared medium.
Examples are Frequency Division Multiplexing and Time Division Multiplexing.
Multiple access allows several users connected to the same medium to transmit over it and
to share its capacity. This is based on multiplexing. It uses the MAC and is controlled
by the data link layer.
Examples are Frequency Division Multiple Access and Time Division Multiple Access.
Practically things like a wireless networks, bus networks and so on.

• How do these terms relate to the duplex, half-duplex, or simplex properties of particular network technologies?

Multiple access networks operate in half-duplex mode using point-to-point links. Cellular
networks combine the use of frequency division duplex to prevent interference.
A simplex connection would be quite useless.

Problem 5.2: Hamming-Code	1+2+2 = 5 points
Two entities have agreed to use the following encoding to transmit characters: Character Code Word A 10000
B 01000
C 11000
D 00100
 . . . . . .
Z 01011
1. How many check bits are required to correct all 1-bit errors in messages with a length of m bits?
2⁵ data words
m + r + 1 < 2^r
5 + 4 + 1 < 2⁴ w.A.
4 bits are required
2. A Hamming Code with 4 check bits shall be used in the following. Create the code words which represent the word HAMMING.

	Data bits	1	2	3	4	5	6	7	8	9
H	00010	1	1	0	1	0	0	1	0	0
A	10000	1	1	1	0	0	0	0	0	0
M	10110	0	1	1	0	0	1	1	0	0
M	10110	0	1	1	0	0	1	1	0	0
I	10010	0	0	1	1	0	0	1	0	0
N	01110	0	0	0	1	1	1	1	0	0
G	11100	0	0	1	0	1	1	0	0	0

3. Consider the following code words have been received:
Decode this sequence, mark the blocks that contain an error, and correct the errors if possible.

not matching paritiy bits are white:
Data bits	1	2	3	4	5	6	7	8	9
	0	1	0	1	0	1	0	0	0
	1	1	1	0	0	1	0	0	0
	0	1	0	1	0	1	0	0	1
	0	0	1	0	1	1	0	0	0
	1	1	1	1	1	1	1	0	0
	0	0	1	0	0	1	1	0	0

Corrected version:
	Data bits	1	2	3	4	5	6	7	8	9
D	00100	0	1	0	1	0	1	0	0	0
A	10000	1	1	1	0	0	0	0	0	0
D	00100	0	1	0	1	0	1	0	0	0
G	11100	0	0	1	0	1	1	0	0	0
O	11110	1	1	1	1	1	1	1	0	0
M	10110	0	0	1	0	0	1	1	0	0

 It is not possible to resolve the last error. It is more than a 1-bit-error.

Problem 5.3: Generator Polynomial	4 × 1 = 4 points
The bit sequence 10100001 has to be transmitted. Use G(x) = x³ + 1 for the generator polynomial of a CRC.
1. Calculate the check sum
10100001000 : 1001 = 10110111
1001
   1100
   1001
     1010
     1001
        1110
        1001
        1110
1001
 1110
 1001
   111
The checksum is 111.
2. Name the bit sequence for the transmission.
10100001111

3. How can the receiver check the correctness of the bit sequence? Show the calculation.
He can check if the remainder of the following calculation is 0.
10100001111 : 1001 = 10110111
1001
   1100
   1001
     1010
     1001
        1111
        1001
        1101
1001
 1001
 1001
       0

4. Assumed there is a bit error on the third bit. Show how the receiver recognizes the error.
10000001111 : 1001 = 1001001
1001
     1000
     1001
        1111
1001
 1101
 1001
   100

There is a remainer which means that there was error.

Problem 5.4: Cyclic Redundancy Checksum	3 points
Determine if the following bit sequences have been transmitted error-free. Use the generator polynomial G to apply a CRC check. G(x) = x⁴ + x + 1 (10011)
If you find an error in a bit sequence, assume that the checksum bits contain the error. Recalculate the checksum.
Data + CRC
1. 0111 0110 0010 : 10011 = 0111111
      100 11
        11 101
        10 011
        1 1100
        1 0011
        1111 0
1001 1
  110 10
  100 11
    10 011
    10 011
     0 → no error

2. 0101 0010 1001 : 10011 = 010111
      100 11
        1 1110
        1 0011
        1101 1
1001 1
  100 00
  100 11
        1101 → error

take only the data bits and recalculate the checksum
0101 0010 0000 : 10011 = 01011
  100 11
      1 1110
      1 0011
        1111 0
        1001 1
        111 10
        100 11
11 010
10 011
  1 0010
  1 0011
1

The correct checksum would be 1.

3. 1111 0110 1100 : 10011 = 111001
    1001 1
      110 11
      100 11
        10 001
        10 011
        100 11
   100 11
0
→ no error

Problem 5.5: CRC in Header or Trailer	1 point
Most data link layer protocols store the CRC value in the trailer rather than the header. Discuss why this is a common approach.

The CRC is computed from the rest of the data package so the trailer can be attached afterwards. Also the receiver reads the data first and checks the correctness later. It simplifies the writing and reading process.

Problem 5.6: LLC vs. MAC	3 points
Discuss the difference tasks of the LLC and MAC.

LLC stands for Logical Link Control. It puts the data into frames and guarantees error free transmission by error detection, flow control and buffer management. The MAC is the access control to the communication channel in broadcast networks. This can be implemented differently depending on the available hardware whereas the LLC is always the same (based on IEEE 802).
The LLC links the network layer to the MAC and ensures that correct information is forwarded. The MAC itself provides addressing and channel access.