Problem 1: (Differential) Manchester 4 points
Consider you have measured the following signal.

The vertical lines represent the end of a bit. Specify the bit sequence that is encoded in the
signal considering that it was encoded with:
1. Manchester baseband encoding (also called biphase-level)
0001101111
2. Differential Manchester
0001011000
Can the bit sequences be specified unambiguously?
For 1. yes but for 2. the first bit could also be a 1 because the previous voltage level is unknown

Problem 2: Data Encoding 5 points
The following bit sequence shall be encoded: 0101110010
Represent the sequence in a time-voltage-diagram using the following encoding schemes:
1. Non-Return-to-Zero (NRZ)

       0 1 0 1 1 1 0 0 1 0
2. Return-to-Zero (RZ)
       0 1 0 1 1 1 0 0 1 0
3. Differential-Non-Return-to-Zero
       0 1 0 1 1 1 0 0 1 0
4. Manchester
       0 1 0 1 1 1 0 0 1 0

5. Differential-Manchester
       0 1 0 1 1 1 0 0 1 0

Problem 3: Manchester Encoding & Bandwidth 3 points
Explain the disadvantage of the Manchester encoding scheme. Propose an improvement!

Only half of the available capacity is used with the Manchester encoding. 1 bit needs 2 bits to be encoded. An improvement would be a 4B/5B code which offers 80% efficiency, meaning that 4 bits are encoded using 5 bits. It uses the differntial NRZ code which indicates a level change with a 1 and no level change with a 0. The other bits encode hexadecimal characters.

Problem 4: Analog to Digital 3 points
Consider a scenario where an analog voice sample has to be transmitted via a digital network.
1. Explain how this can be achieved and which steps are necessary.
The human voice is an analog acoustic signal which is converted to an analog electrical	signal by a microphone. The signal is transferred by a medium i.e. a cable to the receiver	where the analog electrical signal is converted to a analog acoustic signal by a speaker.
2. Discuss the errors that can occur.
The conversion of the signal could be bad so the signal gets lost. Also the analog electrical
signal could be altered by noise. If the initial analog acoustic signal is not strong enough it
may not reach the receiver.
3. Discuss the sampling theorem in this context.
A signal must be sampled at regular intervals at a rate higher than twice the highest	significant signal frequency to obtain all the information of the original signal. This way it
can be ensured that no data gets lost during the conversion of the signal. If the sampling rate
is too low the result will be aliasing and the original signal cannot be reconstructed.

Problem 5: Baud 2 points
1. What is the difference between Baud und Bit/s?
- The symbol rate is the number of signal changes made to the transmission medium per second and is measured in Baud (1/s)
  It is the number of samples per second
- The data rate for binary signals is equal to the symbol rate but for multilevel signals with n possible values the data rate, measured in Bit/s is symbol rate times ld(n)
  It is the amount of information send over the channel.
2. A quaternary digital signal has a symbol rate of v = 10^6 Baud. Is the data rate equal,
smaller or greater than the Symbol rate? Is this allways the case?
The data rate is higher than the symbol rate because in one time step one signal but two bits
encoding the message will be send. This is always the case.
3. For the given signal, what is the data rate?
Data rate = v lg(n) = 10^6 ld(4) = 20^6

Problem 6: Transmission medium used in Ethernet 3 points
1. Which different mediums are used in Ethernet communication?
- Copper (Twisted Pair, coaxial cable)
- Fiber
2. Which medium is the “best” for the given situations?
(a) As primary technology of the Internet’s backbone
Fiber
(b) A dynamic network of moving communication partners
Ethernet is not the right technology at all – a wireless network would be appropriate
Otherwise you could use Twisted Pair
(c) A cheap connection between two nodes which is robust against interference
coaxial cable
(d) A network of many nodes at the same location, in which traffic is produced by a
single node broadcasting to all others
Twisted Pair
(e) A network of many nodes located in an area of a few hundred meters, in which traffic
is produced by a signle node broadcasting to all others
Fiber
(f) A tremendously fast point-to-point connection
Fiber